# UCSB CMS Testing Times

# Modules:  Gantry Operation Timing Summary

| Procedural Step | Approximate Time Required | Comments |
| --- | --- | --- |
| *Database entry of module components. | 10 minutes |  |
| Mount frames on assembly plate (pre-inspected and barcodes attached) | 5 minutes |  |
| Inspect and place sensors on supply plate. | 5 minutes |  |
| Inspect and place hybrids on assembly plate. | 5 minutes |  |
| Mixing glue, loading syringes and applying silver epoxy. | 15 minutes |  |
| Review “before starting gantry program check list” | 2 minutes |  |
| After cure OGP survey of modules (3) | 5 minutes |  |
| Loading modules (3) on to carrier plates. | 8 minutes |  |
| Total Time Total Technician Time | 55 minutes 110 minutes |  |

*While these procedures are being followed, a 45-minute gantry assembly program is run, after which the plates are moved to a curing cabinet.

# Module Wirebonding:  Daily Operation Timing Summary

| Procedural Step | Approximate Time Required | Comments |
| --- | --- | --- |
| Inspect module | 2-3 minutes |  |
| Entering information in database. | 1-2 minutes |  |
| Load the module, wirebond, and unload the module. | 7-8 minutes |  |
| Post-bonding inspection | 2-3 minutes |  |
| Plucking channels that need to be left open | 0-3 minutes |  |
| Store module | 1 minute |  |
| Pull-test and enter information in database. | 5-7 minutes | Performed on every 10th module. |
| Clean wirebonder wedge and recalibrate bonder. | 30-40 minutes | Performed after 10 modules. |
| Total Time Total Technician Time | 20 minutes 20 minutes | *6 chip modules takes slightly longer. |

*The bonding program runs about 30 seconds longer for 6 chip modules, but changing the wirebonder program and the bonding stage for a new type takes about 5-7 minutes.

# Hybrid Wirebonding:  Daily Operation Timing Summary

| Procedural Step | Approximate Time Required | Comments |
| --- | --- | --- |
| Inspect hybrid and clean if necessary | 2-3 minutes |  |
| Enter information in database. | 1-2 minutes |  |
| Load the hybrid, wirebond, and unload the hybrid. | 5-6 minutes |  |
| Post-bonding inspection | 2-3 minutes |  |
| Take hybrid to Test Room | 1 minute |  |
| Pull-test and enter information in database. | 5-7 minutes | Performed on every 10th hybrid. |
| Clean wirebonder wedge and recalibrate bonder. | 30-40 minutes | Performed after 20 hybrids. |
| Total Time Total Technician Time | 15 minutes 15 minutes | Changing the wirebonder program for a new type of hybrid takes about 5-7 minutes. |

# Hybrid Testing:  Daily Operation Timing Summary (First run of the day)

| Procedural Step | Approximate Time Required | Comments |
| --- | --- | --- |
| Initialization procedure | 3 minutes | Only performed at the start of the first run. Involves turning of all equipment and checking for failures. |
| Hybrid Preparation and Mounting | 5 minutes |  |
| Software Procedure Testing Hybrids Cooling cycle Preparation of next batch of 4 Hybrids XML uploading. | 50-55 minutes | Includes XML Uploading Includes cooling cycle of 10-15 minutes. This run is the slowest due to high temperature of cooling fluid. |
| Close all software. Re–start datasocket as well as ACDC. Unload Hybrids and mount prepared Hybrids for next run | 2 –3 minutes |  |
| Total Time Total Technician Time | 1 hour 6 mins |  |

# Hybrid Testing:  Daily Operation Timing Summary (Regular runs after the first)

| Procedural Step | Approximate Time Required | Comments |
| --- | --- | --- |
| Exchanging prepared for finished hybrids | 5 minutes |  |
| Software Procedure Testing Hybrids Cooling cycle Preparation of next batch of 4 Hybrids XML Generation Procedure Unplate the 4 tested Hybrids, label, Place in boxes and store in Cabinet | 45-50 minutes | Includes XML Uploading Includes cooling cycle of 10-15 minutes. Includes the preparation of the next run. |
| Total Time Total Technician Time | 55 mins |  |

# Module Testing:  Daily Operation Timing Summary

| Procedural Step | Approximate Time Required | Comments |
| --- | --- | --- |
| Load module into clamshell, make connections, power on | 1 minute |  |
| Download Checklist | 1 minute |  |
| Run ARCS test * | 22 minutes | During this time, next module can be prepared for testing (including adding test tails), and test area can be maintained. |
| Upload Checklist | 1 minute |  |
| Unload module from clamshell and store. | 1 minute |  |
| Switching between TOB-TEC. | 3 minutes | Performed a few times each day. |
| Database upload of test results and data handling. | 0 | Done automatically once per day. No man-time needed. |
| Total Time Total Technician Time | 20 minutes 20 minutes |  |

* Because of time available during ARCS testing time, it is possible to run two stands with one person.  However, this is not recommended for long periods of time.

# Daily Wien Box Operation Timing Summary

| Procedural Step | Approximate Time Required | Comments |
| --- | --- | --- |
| Quick visual inspection of overnight run. Record pertinent information from LT | 5 min |  |
| Begin analysis of overnight run. Load box for day run. | 30 min 20 min | Done simultaneously |
| Day Run (5 modules) Periodically check progression of run Check validity of night run analysis. Review any modules flagged by lt.pl | 6 hours 1 hour | Done simultaneously |
| Begin analysis of day run data. Reload box for night run. | 15-20 min 20 min | Done simultaneously |
| Overnight Run (10 modules) Check validity of day run analysis. Review any modules flagged by lt.pl | 11+ hr. 30 min | Done simultaneously Sometimes takes longer depending on quality of run. |
| Total Time Total Technician Time | 18 hours 2.5 hours | Varies depending on quality of run. |

*Currently testing 15 modules.  This can be increased to 16 modules per day with minimal changes.  Each additional module will require an extra hour of time either one hour earlier in the morning, or one hour later in the afternoon.

# SS Rod Assembly:  Daily Operation Timing Summary

| Procedural Step | Approximate Time Required | Comments |
| --- | --- | --- |
| Database Entry | 5 minutes |  |
| Dismount rod from shipping box and mount in rotissery | 5 minutes |  |
| Place module on the rod Install screws, make electrical connections and tape HV wire | 7 minutes 5 minutes | Repeat this step 6 times, i.e. a total of 72 minutes |
| Glue the HV tails to CF frame. | 20 minutes |  |
| Cure epoxy | 2 hours |  |
| Total Procedure Time Total Technician Time | 3 hours 42 mins 1 hour 42 mins | Includes curing time |

# DS Rod Assembly:  Daily Operation Timing Summary

| Procedural Step | Approximate Time Required | Comments |
| --- | --- | --- |
| Database Entry | 8 minutes |  |
| Dismount rod from shipping box and mount in rotissery. | 5 minutes |  |
| Place r-phi module on the rod. Place stereo module on the rod. Install screws, make electrical connections and tape HV wire. | 7 minutes 7 minutes 7 minutes | Repeat this step 6 times, i.e. a total of 72 minutes |
| Glue the HV tails to CF frame. | 25 minutes |  |
| Cure epoxy | 2 hours |  |
| Total Procedure Time Total Technician Time | 4 hours 41 mins 2 hours 41 mins | Includes curing time |

# Multi Rod Testing:  Daily Operation Timing Summary

| Procedural Step | Approximate Time Required | Comments |
| --- | --- | --- |
| Load Rods | 1.5 hours |  |
| Unload Rods | 1.5 hours |  |
| Software | 1 hour |  |
| Total Time Total Technician Time | 4 hours 4 hours | A Single Rod Test takes 45 minutes. |