Hybrid wirebonding Certification

( The following individuals can train others in the proper procedures

for hybrid wirebonding.

Susanne Kyre

Kirsten Affolder

( The following individuals have been trained in the hybrid wirebonding procedures by someone authorized to do so in the list above.

| Trainee | Trainer Authorization | Date |
| --- | --- | --- |

HYBRID WIREBONDING PROCEDURE

- Wear grounding straps, lab coat, hat and face mask

- Check that the correct bonding stage is mounted on the wirebonder lab jack at the correct height

- Every morning a USG calibration needs to be performed

- Load the correct bonding program

  - If a new program has been loaded, check the bonding parameters (see separate checklist)

- Check that there is enough wire on the spool

- Check that the wedge is threaded and clean. If the wedge needs to be cleaned, a full calibration needs to be done before bonding. The wedge needs to be cleaned every 30,000 bonds, it needs to be replaced every 300,000 bonds.

- Get the hybrid box from the “unbonded hybrids” cabinet

- Take the hybrid out of the box (hybrid is mounted on carrier plate)

- Inspect the P.A. for excessive dust and clean it with isopropanol and a foam swab if necessary

- Scan the barcode and start the database

- Set the hybrid carrier onto the wire bonding stage and turn the lever to clamp the carrier to the stage

- Check the number of bonds made thus far with the tool and enter them into the database

- Start the bonding program (the program bonds 6 test bonds, 4 bias bonds and all the signal bonds)

  - Watch while the machine is bonding to stop it when wires are missed, missing wire detector is set to 5 bonds

  - If a wire is missed, remove the wiretail, note the number of missed bonds for entry in database

  - If more than 3 bonds are missed, stop the program and remove the part from the machine, put the part aside for later evaluation (reject or try to adjust bonding parameters by doing pulltests)

- If any bonds were left unbonded, go back and rebond

- Release the clamping lever and remove the hybrid carrier from the wire bonding stage

- Place the hybrid carrier under the stereoscope and check the bonds for shorts

- Fix shorts if necessary

- For every 10th part:

  - Place the hybrid carrier on the pull tester

  - Pull test the P.A. test structure bonds

- Put the hybrid carrier back into its box

- Put the box back in the “hybrids ready for testing” cabinet

- Enter the pull test results, number of missed wires and all other information into the database