Hybrid Tailing Certification

( The following individuals can train others in the proper procedures

for hybrid tailing:

Derek Barge

( The following individuals have been trained in the hybrid handling

procedures by someone authorized to do so in the list above.

| Trainee | Trainer Autherization | Date |
| --- | --- | --- |

# General Cleanliness

1) Hands:

- Gloves or finger cots must be used whenever a hybrid is

touched. DO NOT touch any part of any hybrid with a part

of your hand that is not protected by gloves or finger cots.

2) Face & Hair:

- A face mask must be worn at all times while handling hybrids,

and at all times working near an exposed hybrid (an exposed

hybrid is one that is not in a sealed hybrid box). The face mask

must fully cover the mouth and nose.

- A hairnet must be worn inside the clean rooms at all times.

3) Feet:

- Clean booties must be worn inside the clean rooms at all times.

- Grounding straps must be worn any time a hybrid is being

handled. Contact must be checked at a DESCO ‘touch tester’

or at the large DESCO ‘WRIST STRAP / FOOTWEAR tester’ in

the main clean room before handling hybrids.

3) Body:

- A lab coat must be worn inside the clean rooms at all times.

Make sure your lab coat was designed for clean room use.

# Hybrid Tailing Procedure

- If anything does not go according to this procedure, or you are

unsure about what you are doing, stop immediately and contact a

supervisor. DO NOT continute to work until a supervisor is available.

*This procedure should be completed without touching the hybrid at all

*No tools, fingers, or other objects should be held directly above the

hybrid at any time.

1) Check to make sure you are wearing the following:

- booties

- gloves

- hairnet

- lab coat

- face mask

- grounding straps

2) Carefully remove the hybrid from the hybrid box to the work surface.

3) Inspect the hybrid

- For hybrids with ‘up’ connectors, plated hybrids should look like this:

- For hybrids with ‘down’ connectors, plated hybrids should look like this:

- Notice that the upper tail strap is not used for hybrids with ‘Down’

connectors

- If hybrids are encountered that do not look like this, set them

aside and notify a supervisor.

4) Carefully, attach the hybrid tail.

- For hybrids with up connectors, firmly press the test tail straight

down into the hybrid connector:

- For hybrids with down connectors, place the test tail directly underneath the

hybrid connector and press straight down on the hybrid connector:

5) Carefully attach the bottom tail strap.

- Hybrids with ‘Up’ connectors:

- Hybrids with ‘Down’ connectors:

6) Place hybrid in box. Make sure to transfer any and all labels from the original box

to the new box. The hybrid is now ready for thermal cycling on the 4 Hybrid test

stand.

- Hybrids with ‘Up’ connectors should look like this:

- Hybrids with ‘Down’ connectors should look like this: