Module Wirebonding Certification

( The following individuals can train others in the proper procedures

for module wirebonding.

Susanne Kyre

Julie Stoner

( The following individuals have been trained in the module wirebonding procedures by someone authorized to do so in the list above.

| Trainee | Trainer Authorization | Date |
| --- | --- | --- |
| Kirsten Affolder |  | 02/05 |

MODULE WIREBONDING PROCEDURE

- Wear grounding straps, lab coat, hat and face mask

- Check that the correct bonding stage is mounted on the wirebonder lab jack at the correct height

- Every morning a USG calibration needs to be performed

- Load the correct bonding program

  - If a new program has been loaded, check the bonding parameters (see separate checklist)

- Check that there is enough wire on the spool

- Check that the wedge is threaded and clean. If the wedge needs to be cleaned, a full calibration needs to be done before bonding. The wedge needs to be cleaned every 30,000 bonds, it needs to be replaced every 300,000 bonds.

- Get the module box from the “unbonded modules” cabinet

- Take the module carrier out of the box

- Inspect the P.A. for excessive dust and clean it with isopropanol and a foam swab if necessary

- Index the wirebonder stage out and set the module carrier onto the wire bonding stage

- Remove the white clamps form the CF-frame and turn on the vacuum

- Scan the barcode and start the database

- Index the stage back in

- Check the number of bonds made thus far with the tool and enter them into the database

- Start the bonding program (the program bonds 6 test bonds, all bias bonds and all the signal bonds)

  - Watch while the machine is bonding to stop it when wires are missed, missing wire detector is set to 5 bonds

  - If a wire is missed, remove the wiretail, note the number of missed bonds for entry in database

  - If more than 3 bonds are missed, stop the program and remove the part from the machine, put the part aside for later evaluation (reject or try to adjust bonding parameters by doing pulltests)

- If any bonds were left unbonded, go back and rebond

- Index the stage out, turn off the vacuum and push the relief valve button

- Place the white clamps back on the CF-frame and remove the module carrier from the wire bonding stage

- Place the module carrier under the stereoscope and check the bonds for shorts

- Fix shorts if necessary

- For every 10th part:

  - Place the module carrier on the pull tester

  - Pull test the P.A. test structure bonds

- Put the module carrier back into its box

- Put the box in the “modules ready for testing” cabinet

- Enter the pull test results, number of missed wires and all other information into the database