TEC Module Tailing Certification

( The following individuals can train others in the proper procedures

for TEC module tailing.

Derek Barge

( The following individuals have been trained in the hybrid handling

procedures by someone authorized to do so in the list above.

| Trainee | Trainer Authorization | Date |
| --- | --- | --- |

# I. General Cleanliness

1) Hands:

- Gloves or finger cots must be used whenever a hybrid is

touched. DO NOT touch any part of any hybrid with a part

of your hand that is not protected by gloves or finger cots.

2) Face & Hair:

- A face mask must be worn at all times while handling hybrids,

and at all times working near an exposed hybrid (an exposed

hybrid is one that is not in a sealed hybrid box). The face mask

must fully cover the mouth and nose.

- A hairnet must be worn inside the clean rooms at all times.

3) Feet:

- Clean booties must be worn inside the clean rooms at all times.

- Grounding straps must be worn any time a hybrid is being

handled. Contact must be checked at a DESCO ‘touch tester’

or at the large DESCO ‘WRIST STRAP / FOOTWEAR tester’ in

the main clean room before handling hybrids.

4) Body:

- A lab coat must be worn inside the clean rooms at all times.

Make sure your lab coat was designed for clean room use.

# TEC Module Tailing Procedure

- If anything does not go according to this procedure, or you are

unsure about what you are doing, stop immediately and contact a

supervisor. DO NOT continue to work until a supervisor is available.

*This procedure should be completed after module bonding and before ARCS testing.

*No tools, fingers, or other objects should be held directly above the

module at any time.

1) Remove the high voltage guard and place in proper bin.

2) If the module is a R5 Stereo, R6, or R7, carefully secure the high voltage clamp.

Do not clamp the high voltage on R5 modules. There is a clamp for R5 Stereo and

a different clamp that works with R6 and R7, make sure to choose the correct

clamp from the labeled bins.

- Example for R5 Stereo, R6 and R7:

- Example for R5 modules:

3) If the hybrid has an up connector, carefully secure the upper low voltage clamp.

Otherwise proceed to step 4.

- Example for R5 Stereo, R6, and R7:

- Example for R5 modules:

4) Attach the hybrid test tail.

- Example of a TEC module with an ‘Up’ connector:

- Example of a TEC module with a ‘Down’ connector:

5) Carefully secure the lower low voltage clamp.

- Example of a TEC module with an ‘Up’ connector:

- Example of a TEC module with a ‘Down’ connector:

6) The module is now ready for ARCS testing. Place the module on the proper shelf

in the cabinet labeled ‘ARCS TESTING MODULES’.