TEC Module Un-Tailing Certification

( The following individuals can train others in the proper procedures

for TEC module Un-Tailing.

Derek Barge

( The following individuals have been trained in the hybrid handling

procedures by someone authorized to do so in the list above.

| Trainee | Trainer Authorization | Date |
| --- | --- | --- |

# I. General Cleanliness

1) Hands:

- Gloves or finger cots must be used whenever a hybrid is

touched. DO NOT touch any part of any hybrid with a part

of your hand that is not protected by gloves or finger cots.

2) Face & Hair:

- A face mask must be worn at all times while handling hybrids,

and at all times working near an exposed hybrid (an exposed

hybrid is one that is not in a sealed hybrid box). The face mask

must fully cover the mouth and nose.

- A hairnet must be worn inside the clean rooms at all times.

3) Feet:

- Clean booties must be worn inside the clean rooms at all times.

- Grounding straps must be worn any time a hybrid is being

handled. Contact must be checked at a DESCO ‘touch tester’

or at the large DESCO ‘WRIST STRAP / FOOTWEAR tester’ in

the main clean room before handling hybrids.

4) Body:

- A lab coat must be worn inside the clean rooms at all times.

Make sure your lab coat was designed for clean room use.

# TEC Module Un-Tailing Procedure

- If anything does not go according to this procedure, or you are

unsure about what you are doing, stop immediately and contact a

supervisor. DO NOT continute to work until a supervisor is available.

*No tools, fingers, or other objects should be held directly above the

module at any time.

- Example of TEC module with ‘Up’ connector:

- Example of TEC module with ‘Down’ connector:

1) If the a high voltage clamp is present, carefully remove the high voltage clamp.

2) Carefully remove the lower low voltage clamp.

3) Cautiously, remove the hybrid tail. Follow a) for R5 Stereo, R6, and R7, and

b) for R5 modules. Use a flat head jewlers screw driver with a 1/8"

blade.

a) R5 Stereo, R6, and R7 modules

- Take a small flat head jewelers screw driver and place the edge

of the flat head in the top seam between the hybrid connector and

the test tail. Make sure not to pry the connector mounted

on the hybrid tail against the hybrid tail.

- Rotate the driver 90(, this will free one side of the connector.

- Very gently push down on the SAME SIDE side of the connector

that was just freed in the upper right hand corner, this should release the test tail

from the connector.

- If the test tail does not come completely free, gently grasp both ends and

gently wiggle it free. There should be very little to no resistance.

- Gently remove the hybrid tail.

b) R5 modules

* Examples shown are with TEC hybrid only, but the procedure is no different

for a TEC module.

- Take a small flat head jewelers screw driver and place the edge

of the flat head in the bottom seam between the hybrid connector and

the test tail. Make sure not to pry the connector mounted

on the hybrid tail against the hybrid tail.

- Rotate the driver 90(, this will free one side of the connector.

- Very gently push down on the SAME SIDE side of the hybrid tail that was

just freed in the upper right hand corner, this should release the connector

from the test tail.

- If the hybrid tail does not come completely free, gently grasp both ends and

gently wiggle it free. There should be very little to no resistance.

- Gently remove the hybrid tail from the test tail and remove test tail.

5) If the module has an ‘Up’ connector, carefully remove the upper low voltage

clamp.

- Example of finished TEC module with ‘Up’ connector:

- Example of finished TEC module with ‘Down connector:

7) Place on proper shelf in ‘LT TESTING MODULES’ cabinet.