## Slide 1: The LZ Liquid Scintillator Screener Campaign
Scott Haselschwardt, for the LZ Collaboration
CoSSURF 2017
May 13, 2017

## Slide 2: The LZ Experiment
Veto PMTs Inside Tyvek Curtain
Central TPC,
7 tonnes LXe,
494 3” PMTs
High Voltage Feedthrough
DD Neutron Calibration Tubes
Xenon Handling Lines
Liquid Scintillator “Outer Detector” Veto
Former LUX Water Tank

## Slide 3: The LZ Outer Detector
9 segmented UVT acrylic tanks
~17 tonnes Gd-loaded, LAB-based LS
  Neutrons thermalize and capture on Gd:
  n + Gd -> Gd + (3-4x)γ(~8 MeV)
120 8” PMTs in water tank
  Surrounded by Tyvek reflector
Together with LXe “skin”, veto gammas and neutrons with high efficiency… 100-200 keV threshold
Reduce WIMP search backgrounds
Simulated neutron background in LZ before and after application of veto cuts

## Slide 4: GdLS Purity
OD rate goal drives scintillator purity requirements
Usual suspects: 238U, 232Th & 40K
14C a main concern
  LLNL Mass Spec down to 10-15 g/g
  Requirement/goal is 10-17-10-18 g/g
Impurity | Goal | Requirement
238U | 1.3 ppt | 10 ppt
232Th | 4.5 ppt | 20 ppt
40K | 0.8 ppt | 3 ppt
14C | 1.3 x 10-17 g/g | 1.5 x 10-17 g/g

## Slide 5: The LS Screener
Made of Reynolds UVT acrylic (same as OD)
~ 24 kg GdLS
  ~1/700 of OD LS
  Produced by Minfang Yeh at BNL
14 kg water shield
3 R11410-20 PMTs
  Very radiopure
  LZ PMT bases
Wrapped in Tyvek reflector
GdLS
Water

## Slide 6: Underground Commissioning, Nov. 2016
GdLS filling in underground cleanroom
Water volume full, mounting PMTs

## Slide 7: Ready for Water Tank Deployment
Teflon tube for thoron calibration
Filled w/ GdLS and water. PMTs mounted:
Wrapped in single layer tyvek, ready for deployment:

## Slide 8: Water Tank Deployment

## Slide 9: Data Taking Overview
Deployed in LUX water shield
  LUX support stand still present
Pulses amplified & digitized by LZ electronics
Run 1: GdLS
  Mid Nov 2016 – Early Jan 2017
Run2: No Gd-loading
  Late Jan 2017 – Late Feb 2017
~Weekly PMT gain monitor
Calibrations end each run:
  γ: 137Cs, 22Na, 40K, 228Th
  α&β: Thoron bubbling
End of each run “z-scan”

## Slide 10: Run 1 – First Data
We see α’s, β’s and Compton deposits from ɣ’s
Rate plateau after ~ 3 weeks
0.25 phe/keV  3-fold coinc of > 2 phe  24 keV threshold
Acceptance for ~70% of 14C beta spectrum
Radon α peak decays…
U, Th α’s leftover
14C + 152Gd α

## Slide 11: Run 2 – No Gd
Same cocktail without Gd
Less exposure during LS fill
Rate plateau after ~ 2 weeks
Higher light yield, ~0.3 phe/keV
14C, no Gd
Radon α peak decays…
U, Th α’s leftover

## Slide 12: End of Run Z-Scan
Rate in OD from cavern environment a concern
End of each run, moved Screener vertically
Top of OD acrylic….
4-5x lower than sim!
OD bottom
OD top
Wanted to probe here!
Low rate spot

## Slide 13: Background Simulations
Detailed geometry in Geant4-based LUXSim code
U, Th, K and Co simulated in:
  Tyvek
  Ropes
  Titanium Ballast
  PMTs and bases
  PMT mounting structures
  PMT cabling
  Flange bolts
  Acrylic vessel
  LUX support stand
  Davis Cavern rock
In LS volume: U, Th, K, 14C and 152Gd
Direct screening results or LZ database for normalizations

## Slide 14: First Fit to Run 1 Data
Simulated spectra -> RooFit PDFs grouped by internal or external to LS
Constraints: External U, Th, K & Co from counting, 152Gd rate from known concentration & late chain U & Th from BiPo rate
Preliminary

## Slide 15: Impurity Estimates from Run 1
Close to requirement on 14C
  Crude fit to Run 2 within factor of 2
U, Th okay…
  Evidence for non-equilibriated sub-chains
  HPGe screening of GdCl3 underway
40K expected to drop with updated fit
Impurity | Level Estimate | Comes From | Goal | Requirement
238U | 6.5 ± 1.5 ppt early 3.1 ± 0.3 ppt late | Fit early, BiPo late | 1.3 ppt | 10 ppt
232Th | 22 ± 5 ppt early 1.3 ± 0.4 ppt late | Fit early, BiPo late | 4.5 ppt | 20 ppt
40K | 12 ± 1 ppt | Fit | 0.8 ppt | 3 ppt
14C | (2.7 ± 0.1) x 10-17 g/g | Fit | 1.3 x 10-17 g/g | 1.5 x 10-17 g/g

## Slide 16: Next Steps
Run 2 fits
Pulse shape discrimination
  Constrain U & Th alphas
Z-scan analysis
Mix of U and Th α’s

## Slide 17: Conclusions
Screener campaign a success!
Providing useful feedback to LZ
  Operational experience with GdLS
  GdLS production modifications for lower backgrounds
We are close to our purity requirements for the GdLS
Z-scan constrain Davis Cavern gamma rate

## Slide 18: Thank You!
Simon Fiorucci
Markus Horn
Dave Taylor
SURF personnel
U. Rochester
Brown U.
U. Davis
LZ Screening Crew
Dean White
Susanne Kyre
Harry Nelson
Mike Witherell
Curt Nehrkorn
Melih Solmaz
Sally Shaw
Minfang Yeh

## Slide 19: Extra Slides

## Slide 20: Thoron Calibration
Bubble N2 past 228Th source into LS
Vents through concentric tubing to bubbler outside water tank
Testing at UCSB

## Slide 21: 1.06.04 – Gd-LS Impurities 2/20/2017
Component | Raw Values (ppt) |  |  |  | Gram per Liter Gd-LS | 0.1% Gd-LS in veto (ppt) |  |  | 
 | 238U | 232Th | 40K | 14C |  | 238U | 232Th | 40K | 14C
LAB | 0.004 | 0.007 | 0.5 | 12 × 10-6 | 860 | 0.004 | 0.007 | 0.5 | 12 × 10-6
Gd | 100 | 100 | 52 |  | 0.86 | 0.17 | 0.17 | 0.09 | 
PPO | 150 | 640 | 27 | 110 × 10-6 | 3 | 0.5 | 2.2 | 0.09 | 0.37 ×10-6
TMHA | 180 | 650 | 27 | 140 × 10-6 | 3 | 0.6 | 2.1 | 0.09 | 0.44 ×10-6
bis-MSB | 210 | 190 | 50 | 19 × 10-3 | 0.015 | 0.004 | 0.003 | 0.001 | 0.32 ×10-6
Total/Goal |  |  |  |  | 867.2 | 1.3 (≈3.1BiPo) | 4.5 | 0.8 | 13 (≈27)×10-6
Rate (Hz) |  |  |  |  |  | 3.75 | 3.75 | 3.75 | 3.75
Requirement |  |  |  |  |  | 10 | 20 | 3 | 15 × 10-6
Rate (Hz) |  |  |  |  |  | 30 | 17 | 14 | 4.3
Daya Bay |  |  |  |  |  | 20 | 4 | 7 | 
Daya Bay levels from one-pass purification of Gd and PPO; 40K from water or contamination
85Kr – if like KAMLAND, <20 counts per day
Yellow are measurements (ICPMS/HPGe), blue screener